## Slide 1: Green Corps 2017

## Slide 2: Learning to play guitar

## Slide 3: MIDS calculator
An Excel spreadsheet that
  quantifies reductions in stormwater runoff volume for a given BMP or group of BMPs
  quantifies reductions in phosphorus (P) and TSS in stormwater runoff for a given BMP or group of BMPs
  can be used to determine and size best BMP(s) for a particular situation
Has a Graphical User Interface (GUI)

## Slide 4: Why do we need to know these?
Meet regulatory requirements
Meet water quality targets
Choose most efficient/effective BMP

## Slide 5: Who uses it?
Engineers for project sites
Technical staff at watershed organizations and other Local Government Units (LGUs)
People seeking funding for projects
Educators
Etc. – we can’t track all users, but Version 3 has been downloaded 2500 times this year

## Slide 6: How does it work?
Calculate the amount of stormwater runoff, P, and TSS entering the BMP
Different BMPs have removal efficiencies based on research and monitoring
Calculator does a mass balance on volume, P, and TSS coming in, being removed, and returning as runoff

## Slide 7
100% TSS, PP, DP reduction
Overflow volume
0% TSS, Particulate P (PP),
and Dissolved P (DP)
reduction
Infiltration BMPs
100% TSS, PP, DP reduction
Filtered volume
60% TSS. Particulate P (PP),
and Dissolved P (DP)
Calculated based on media
Filtration BMPs w/ some infiltration
Settled solids
Settled solids
90% TSS and associated pollutants,
No removal of dissolved pollutants
Sedimentation BMPs
No infiltration

## Slide 8
Green Roof
Bioretention Basin
Infiltration Basin
Permeable Pavement
Swale Side Slope
Swale Main Channel
Wet Swale
Swale With Underdrain
The BMPs

## Slide 9
Sand Filter
Stormwater Pond
Stormwater Pond w/ Filter Bench
Wetland
Other
Other
Harvest and Reuse
Impervious Disconnect
Bioretention Basin with underdrain
Tree trench

## Slide 10
Underground Infiltration
Tree trench with underdrain

## Slide 11: Examples
2 acre site
  1 acre impervious
  1 acre pervious turf
B soils
Zip = 55105
Goals
  Infiltrate first 1.1 inches off impervious surfaces
  Capture 80 percent of Total P

## Slide 12: Problem 1: Same as example but pick one of these conditions
Have to minimize surface space of the BMP
½ the impervious is parking lot
The full acre of impervious is a linear road
You are on a C soil
½ the impervious is a building roof

## Slide 13: Treatment train
Multiple BMPs used in series
Route excess water from one BMP to the next

## Slide 14: Problem 2
10 acre site, half is pervious forest and half is impervious
  Impervious: 1 acre on A soils, 2 acres on B soils, 2 on D soils
  Pervious acreage: same as impervious
Goal is to meet the MN Construction SW Permit – infiltrate first 1 inch off impervious surfaces
Hints: draw a site map; you’ll probably need or want multiple BMPs; include treatment train on your map
Pick your zip code